Updated RDO install steps as of 2025 – caracal version – centos 9 stream:
Packstack - An OpenStack distribution
Step 0: Install CentOS 9 Stream
Do Manual partitioning
  - /boot: 30-40GB
  - /SWAP: 2*mem (50-60 GB is also fine though)
  - /home: 30GB
  - /: rest storage (/var will come in this only)
  - biosboot: 1MB
Install timeshift to have a backup snapshot before making any changes, for reverting in case any issues arise.
sudo dnf install epel-release
dnf update
dnf install timeshift
timeshift --create --comments "Initial backup"
Step 1: Set up hostname and static IP to the machine

- Provided (to set static IP via #nmtui-edit eth160):
  - IP ADDRESS : 172.24.35.26/20
  - GATEWAY: 172.24.32.1
  - DNS:
    - <DNS IP>
  - Search Domains:
    - <DNS SEARCH SUFFIX>

systemctl restart NetworkManager
sudo nmcli con modify eno1 ipv4.addresses 172.24.29.132/20
sudo nmcli con modify eno1 ipv4.gateway 172.24.16.1
sudo nmcli con modify eno1 ipv4.dns "<DNS IP>"
sudo nmcli con modify eno1 ipv4.method manual
sudo nmcli con down eno1 && sudo nmcli con up eno1

Step 2: Attach 500GB volume and Create a VG named ‘cinder-volumes ‘ on /dev/sdb
# in this case I have 2.7TB VG, so will use 2TB for cinder size.
vgcreate cinder-volumes /dev/sdb

Step 3: Pre-requisites
sudo dnf update -y

sudo setenforce 0      # Disable SELinux temporarily
OR
Set SELINUX=disabled in /etc/selinux/config and reboot the VM
***If network doesn’t start properly after reboot, run these 2 again.
nmcli con mod eno1 ipv4.addresses 172.24.29.132/20
nmcli con down eno1 && nmcli con up eno1

sudo hostnamectl set-hostname rdo-openstack
echo "172.24.29.132 rdo-openstack" >> /etc/hosts
sudo systemctl disable firewalld
sudo systemctl stop firewalld

Step 4: Install openstack and packstack packages
sudo dnf install -y centos-release-openstack-caracal
sudo dnf config-manager --enable crb
dnf install -y openstack-packstack

Step 5: Configure network bridge
nmcli connection add type ovs-bridge conn.interface br-ex
nmcli connection add type ovs-port conn.interface eno1 master br-ex
# when you created the OVS bridge, NetworkManager automatically named the connection something like ovs-bridge-br-ex, not just br-ex.
nmcli connection show
nmcli connection modify ovs-bridge-br-ex ipv4.addresses 172.24.29.132/20 ipv4.gateway 172.24.16.1 ipv4.method manual ipv4.dns "<DNS IP>"
dnf install openvswitch NetworkManager-ovs -y
systemctl enable openvswitch
systemctl start openvswitch
systemctl restart NetworkManager
nmcli connection up ovs-bridge-br-ex
ovs-vsctl show

Step 6: Run Packstack to configure Openstack
Optional: create another timeshift snapshot.
timeshift --create --comments "Before packstack run"
packstack --install-hosts=172.24.29.132 \
  --provision-demo=n \
  --os-neutron-ml2-type-drivers=vxlan,flat \
  --os-neutron-ml2-mechanism-drivers=openvswitch \
  --os-neutron-l2-agent=openvswitch \
  --os-neutron-ovs-bridge-mappings=extnet:ovs-bridge-br-ex \
  --os-neutron-ovs-bridge-interfaces=ovs-bridge-br-ex:eno1 \
  --os-cinder-install=y \
  --cinder-volumes-create=n \
  --cinder-volumes-size=2048G

………………………………………………………………………………………………………

A provider network in OpenStack is a special type of Neutron network that directly maps to the physical data center network, allowing instances to connect to external infrastructure without tunneling or overlay networks. It’s typically used for giving VMs direct access to existing VLANs or flat networks managed outside OpenStack. A provider network bridges OpenStack instances to the physical network infrastructure (switches/routers). Each provider network maps to a provider bridge (e.g., br-ex) on compute nodes.

In OpenStack networking, a bridge acts like a virtual switch that connects virtual machine (VM) interfaces to physical or external networks. It enables traffic flow between instances, routers, and provider networks by mapping logical networks to physical interfaces through Linux Bridge or Open vSwitch (OVS). A bridge is a Layer-2 construct that forwards Ethernet frames between interfaces, similar to a physical switch. In Linux bridge networking, the "master" is the bridge interface itself, and the "slaves" are the physical or virtual interfaces attached to it. This terminology reflects how traffic is controlled and forwarded: the bridge (master) governs how packets flow between its connected interfaces (slaves). Bridge maintains a MAC address table to forward packets intelligently between ports. Slave interfaces are physical NICs (e.g., eth0) or virtual interfaces (e.g., tapXYZ) that are enslaved to the bridge. These interfaces don’t have IP addresses themselves — the bridge holds the IP. They simply pass traffic to and from the bridge.

Linux Bridge:
- Simple kernel-based bridge.
- Often used in smaller or performance-focused deployments.
- Provides VLAN tagging and basic isolation.
Open vSwitch (OVS):
- More advanced, supports tunneling (VXLAN, GRE), VLANs, and SDN integration.
- Common in large-scale or multi-tenant OpenStack clouds.

Bridge mappings associate a network label with a bridge device. Example: extnet:ovs-bridge-br-ex
Here, the logical label extnet is mapped to the external bridge br-ex. This allows provider network traffic to leave the virtual environment and reach the physical network.

--os-neutron-ml2-type-drivers=vxlan,flat → Enables two types of networks:
- VXLAN → for tenant (overlay) networks. isolated per project
- Flat → for provider networks (direct mapping to physical) giving external connectivity.

--os-neutron-ml2-mechanism-drivers=openvswitch → Using OVS as the switching backend.

--os-neutron-ovs-bridge-mappings=extnet:ovs-bridge-br-ex → This is the critical line. It maps the logical label extnet(Neutron’s name for the provider network) to the external bridge ovs-bridge-br-ex. That’s how you define a provider network: you tell Neutron “this physical bridge corresponds to the external network.”
In Neutron, extnet appears as a network object you can attach routers or VMs to. It looks like a “virtual network” in the OpenStack dashboard/CLI. Because of the bridge mapping, extnet is directly tied to the physical external network connected to eno1. Traffic on extnet flows straight out to your data center LAN or upstream router.

--os-neutron-ovs-bridge-interfaces=ovs-bridge-br-ex:eno1 → Binds the external bridge to the host’s physical NIC (eno1). This is what lets VMs reach the outside world directly.

VM NIC inside the guest connects to a tap device on the host.
The tap plugs into the integration bridge (br-int).
From br-int, traffic flows into the virtual router namespace (qrouter).
The router’s external port connects to the provider network (extnet), which is mapped to the external bridge (br-ex).
br-ex is bound to the physical NIC (eno1).
Finally, traffic leaves via the physical router into the external network/Internet.
## Packet Flow: VM → External Network
### 1. VM vNIC (Virtual NIC)
- Inside the VM, the packet originates at its virtual NIC (vNIC).
- The vNIC is backed by a tap device on the hypervisor host (e.g., tapXYZ).
- This tap device is connected to the integration bridge (br-int).
### 2. Integration Bridge (br-int)
- br-int is the central Open vSwitch (OVS) or Linux Bridge where all VM interfaces connect.
- It tags traffic with the appropriate network segmentation ID (VLAN, VXLAN, or GRE).
- If the destination is external, the packet is forwarded toward the virtual router namespace.
### 3. Virtual Router (qrouter namespace)
- Neutron creates a Linux network namespace for each tenant router (qrouter-<UUID>).
- The packet enters the router’s internal interface (connected to br-int).
- The router performs:
  - Routing decision (based on destination IP).
  - NAT (SNAT/DNAT) if floating IPs or external access are involved.
  - Security group rules (iptables or OVS flows).
- The packet exits via the router’s external gateway port, which is connected to the external bridge (br-ex).
### 4. External Bridge (br-ex)
- br-ex is mapped to a physical NIC on the host (e.g., eth0).
- This bridge connects the virtual world to the physical data center network.
- The packet is now ready to leave the hypervisor.
### 5. Host NIC (Physical Interface)
- The packet traverses the host’s physical NIC (e.g., eth0).
- At this point, it’s just a normal Ethernet frame with VLAN tagging or encapsulation removed (depending on provider network setup).
- The NIC sends the packet onto the physical network fabric.
### 6. Physical Router / Switch
- The packet reaches the physical router/switch in the data center.
- This router:
  - Routes the packet toward the external destination (e.g., Internet).
  - Handles ARP resolution, MAC learning, and routing protocols.
- From here, the packet flows out to the external network/Internet.

East-West traffic (VM ↔ VM) may bypass br-ex and stay within br-int if on the same tenant network.
North-South traffic (VM ↔ Internet) always passes through the virtual router and br-ex.

A tap device is a virtual network interface created on the hypervisor host for each VM. Think of it as the host-side endpoint of the VM’s vNIC. When a VM boots, OpenStack (via libvirt/QEMU) creates a tap device like tap123abc. That tap device is then connected to a bridge (Linux Bridge or OVS). If your VM has an interface eth0 inside the guest, the hypervisor creates a corresponding tapXYZ device on the host. Packets leaving the VM’s eth0 appear on tapXYZ. Tap device doesnt have IP as its just a layer 2 endpoint. Its only job is to forward Ethernet frames between the VM and the host’s bridge (br-int). VM NIC inside the VM does have an IP.

The integration bridge (br-int) is a virtual switch inside the host. It’s part of Open vSwitch (OVS) or Linux Bridge, depending on your deployment. All VM tap devices plug into br-int.
Acts as the central switching fabric for tenant networks. Without br-int, VM interfaces would be isolated and unable to talk to each other or external networks.

### VM A wants to send data to VM B
1. ARP Resolution:
  1. Machine A knows VM B’s IP.
  2. It sends an ARP request: “Who has IP 192.168.1.10?”
  3. The bridge (master) forwards this to all slaves.
  4. VM B replies with its MAC address.
2. MAC Learning:
  1. The bridge learns: “MAC X is reachable via tapXYZ.”
  2. Now it can forward future frames directly to that tap device.
3. Frame Forwarding:
  1. Machine A sends Ethernet frames to MAC X.
  2. The bridge receives them and forwards to the correct slave (tapXYZ).
  3. VM B receives the data — all without the tap device having an IP.

## External Machine → VM in OpenStack
### 1. External Machine Sends Packet
- Suppose an external client wants to reach a VM at 203.0.113.50 (a floating IP).
- It sends a packet toward that IP.
- The packet travels across the Internet and arrives at the data center’s physical router.
### 2. Physical Router → Host NIC
- The physical router knows that 203.0.113.50 belongs to the OpenStack cloud.
- It forwards the packet into the cloud’s external network segment.
- The packet arrives at the host’s physical NIC (e.g., eth0).
### 3. Host NIC → External Bridge (br-ex)
- The NIC is enslaved to the external bridge (br-ex).
- br-ex is the Layer‑2 switch that connects the host to the external world.
- The packet enters br-ex.
### 4. External Bridge → Virtual Router Namespace (qrouter)
- The VM doesn’t directly own the public IP (203.0.113.50).
- Instead, the virtual router namespace (created by Neutron) owns that IP on its external interface.
- The packet is delivered to the router’s external port inside the namespace.
### 5. Virtual Router: DNAT
- The router performs Destination NAT (DNAT):
  - Maps the floating IP (203.0.113.50) to the VM’s private IP (10.0.0.5).
- Routing decision: “This packet is for 10.0.0.5 on the tenant network.”
### 6. Router → Integration Bridge (br-int)
- The router forwards the packet out its internal interface.
- That interface is connected to the integration bridge (br-int).
- br-int tags/encapsulates the packet for the correct tenant network.
### 7. Integration Bridge → Tap Device
- br-int looks up the MAC address for 10.0.0.5.
- It forwards the packet to the correct tap device (tapXYZ) associated with the VM.
- The tap device is the host-side endpoint of the VM’s NIC.
### 8. Tap Device → VM NIC
- The packet enters the VM through its vNIC (eth0 inside the guest).
- The VM sees the packet as destined for its private IP (10.0.0.5).